SETUP DETAILS

1 compute node, 3/4 storage nodes

Compute node
CPU: 2 * Intel(R) Xeon(R) CPU E5-2650 v2 @ 2.60GHz (8 core, 16 threads)
RAM: (4*16 ) GB per CPU (128 GB total), DIMM DDR3
Storage: 1 * 3.7 TB
Network: single 10Gbps link
Daemons running : mon, radosgw, cosbench

Storage node
CPU: 2 * Intel(R) Xeon(R) CPU E5-2430 v2 @ 2.50GHz (6 core, 12 threads)
RAM: (4*16 ) GB per CPU (128 GB total), DIMM DDR3
Storage: 25 * 3.7 TB
Network: single 10Gbps link
Daemons running per node : 25 osds, 1 mon, 1 radosgws, cosbench

Ceph configuration
ceph version 0.94.3 (95cefea9fd9ab740263bf8bb4796fd864d9afe2b)
Replication factor of 3
No HAProxy, Keystone
Other ceph configuration is as follows :
auth_cluster_required = cephx
auth_service_required = cephx
auth_client_required = cephx
filestore_xattr_use_omap = true
osd_mkfs_options = -f -i size=2048 -n size=64k
osd_mount_options_xfs = inode64,noatime,logbsize=256k
osd_pool_default_pg_num = 2048
osd_pool_default_pgp_num = 2048
filestore_min_sync_interval = 10
filestore_max_sync_interval = 15
filestore_queue_max_ops = 25000
filestore_queue_max_bytes = 10485760
filestore_queue_committing_max_bytes = 10485760000
filestore_op_threads = 64
journal_max_write_bytes = 1073714824
journal_max_write_entries = 10000
journal_queue_max_ops = 50000
journal_queue_max_bytes = 10485760000

rgw cache enabled = false
rgw thread pool size = 1024
rgw num rados handles = 1024
rgw ops log rados = false
rgw print continue = true
debug rgw = 0
rgw enable ops log = false
log to stderr = false
rgw enable usage log = false

objecter inflight op bytes = 1073741824

[osd]
osd_max_write_size = 512
osd_client_message_size_cap = 2048*1024L*1024L
osd_disk_threads = 24
osd_op_threads = 24

BASELINING THE SETUP

Disk
Each of the disk was formatted with filesystem type xfs and mounted with (rw,noatime,inode64,logbsize=256k) options. The journal was on a different partition on the same disk.

Disk writes
Sequential write on single disk using dd : 170 MB/s
Sequential write on single disk using fio : 175 MB/s
Random write on single disk using fio : 135 MB/s
Sequential writes on all disks using dd : 120 MB/s per disk, 3000 MB/s cumulative
Sequential writes on all disks using fio : 125 MB/s per disk, 3125 MB/s cumulative
Random writes on all disks using fio : 120 MB/s per disk, 3000 MB/s cumulative

Disk reads
Sequential read from single disk using dd : 180 MB/s
Sequential read from single disk using fio : 177 MB/s
Random read from single disk using fio : 138 MB/s
Sequential read from all disks using dd : 140 MB/s per disk, 3500 MB/s cumulative
Sequential read from all disks using fio : 135 MB/s per disk, 3375 MB/s cumulative
Random read from all disks using fio : 120 MB/s per disk, 3000 MB/s cumulative

TODO
Journals on SSDs

Network
Using iperf with a single sender on compute node and one receiver one each storage node, we are able to saturate the link and achieve 1.2 Gbits/sec throughput. Some system parameters were also tuned which are as follows:

net.core.rmem_max = 134217728
net.core.wmem_max = 134217728
net.core.rmem_default = 134217728
net.core.wmem_default = 134217728
net.core.optmem_max = 134217728
net.ipv4.tcp_rmem = 4096 87380 67108864
net.ipv4.tcp_wmem = 4096 65536 67108864
net.core.somaxconn = 1024
net.core.netdev_max_backlog = 250000
net.ipv4.tcp_max_syn_backlog = 30000
net.ipv4.tcp_max_tw_buckets = 2000000
net.ipv4.tcp_tw_reuse = 1
net.ipv4.tcp_fin_timeout = 10
net.ipv4.udp_rmem_min = 8192
net.ipv4.udp_wmem_min = 8192
net.ipv4.conf.all.send_redirects = 0
net.ipv4.conf.all.accept_redirects = 0
net.ipv4.conf.all.accept_source_route = 0

TODO
1. Enable jumbo frames across the network
2. Separate public and cluster networks

WRITE PERFORMANCE

3 Storage Nodes

<object size>-<num threads>t	Avg latency using rados gateway and cosbench	Avg latency using rados bench (seconds)	Avg throughput using rados gateway and cosbench	Avg throughput using rados bench (MB/s)
1k-1t	43.1 ms	0.0182498	23.12 KB/S	0.054
1k-4t	49.62 ms	0.0169283	80.33 KB/S	0.231
1k-16t	80.62 ms	0.0268121	198.07 KB/S	0.583
1k-32t	139.04 ms	0.0418749	229.89 KB/S	0.746
1k-64t	285.74 ms	0.0676951	223.86 KB/S	0.92
1k-128t	614.55 ms	0.13963	208.23 KB/S	0.893
64k-1t	59.97 ms	0.0181073	1.06 MB/S	3.451
64k-4t	60.65 ms	0.0173508	4.21 MB/S	14.405
64k-16t	103.5 ms	0.0295197	9.88 MB/S	33.87
64k-32t	178.24 ms	0.0497003	11.48 MB/S	40.236
64k-64t	343.22 ms	0.093766	11.93 MB/S	42.61
64k-128t	690.84 ms	0.175645	11.86 MB/S	45.538
1m-1t	91.79 ms	0.0449231	11.14 MB/S	22.259
1m-4t	93.26 ms	0.0529229	43.85 MB/S	75.565
1m-16t	161.05 ms	0.143823	101.65 MB/S	111.203
1m-32t	286.81 ms	0.225166	114.2 MB/S	141.996
1m-64t	504.96 ms	0.487955	129.75 MB/S	131.099
1m-128t	935.31 ms	0.899171	140.11 MB/S	142.292
16m-1t	215.51 ms	0.252352	75.97 MB/S	63.402
16m-4t	442.95 ms	0.314305	147.9 MB/S	203.617
16m-16t	804.35 ms	0.516217	325.85 MB/S	495.86
16m-32t	1335.56 ms	0.779886	392.5 MB/S	653.388
16m-64t	2390.74 ms	1.34113	438.58 MB/S	761.165
16m-128t	4735.26 ms	2.64825	442.95 MB/S	765.269
64m-1t	643.4 ms	0.770844	101.84 MB/S	83.025
64m-4t	1394.38 ms	0.977854	187.98 MB/S	261.284
64m-16t	2801.25 ms	1.70642	374.31 MB/S	594.598
64m-32t	4939.62 ms	3.31076	424.51 MB/S	606.581
64m-64t	9214.91 ms	6.31811	455.21 MB/S	607.528
64m-128t	17917.56 ms	11.8536	468.23 MB/S	602.539

4 Storage Nodes

<object size>-<num threads>t	Avg latency using rados gateway and cosbench	Avg throughput using rados gateway and cosbench
1k-1t	51.56 ms	19.33 KB/S
1k-4t	54.77 ms	72.8 KB/S
1k-16t	64.57 ms	247.13 KB/S
1k-32t	112.76 ms	283.41 KB/S
1k-64t	243.25 ms	262.87 KB/S
1k-128t	497.15 ms	257.75 KB/S
64k-1t	35.76 ms	1.78 MB/S
64k-4t	37.03 ms	6.88 MB/S
64k-16t	71.95 ms	14.2 MB/S
64k-32t	150.64 ms	13.58 MB/S
64k-64t	296.76 ms	13.8 MB/S
64k-128t	556.42 ms	14.73 MB/S
1m-1t	65.91 ms	15.51 MB/S
1m-4t	65.26 ms	62.64 MB/S
1m-16t	110.61 ms	147.96 MB/S
1m-32t	210.11 ms	155.87 MB/S
1m-64t	394.87 ms	165.92 MB/S
1m-128t	715.58 ms	183.04 MB/S
16m-1t	185.47 ms	88.27 MB/S
16m-4t	394.8 ms	165.94 MB/S
16m-16t	772.33 ms	339.36 MB/S
16m-32t	1150.97 ms	455.48 MB/S
16m-64t	1973.72 ms	531.27 MB/S
16m-128t	3714.35 ms	564.68 MB/S
64m-1t	564.89 ms	115.96 MB/S
64m-4t	1253.7 ms	209.07 MB/S
64m-16t	2375.39 ms	441.4 MB/S
64m-32t	4171.34 ms	502.78 MB/S
64m-64t	7348.31 ms	570.69 MB/S
64m-128t	14299.03 ms	586.66 MB/S

Key Conclusions:
1. Latency and throughput both increases with increase in number of concurrents requests
2. With increase in the number of storage nodes throughput increases and latency decreases.
3. A single rados gateway is able to utilize the cpu, i/o resources of 3/4 storage nodes when the object size is bigger (> 1M).
Note: system wide statistics are available for all of these tests.

READ PERFORMANCE

3 Storage Nodes

<object size>-<num threads>t	Avg latency using rados gateway and cosbench	Avg latency using rados bench (seconds)	Avg throughput using rados gateway and cosbench	Avg throughput using rados bench (MB/s)
1k-1t	63.78 ms	0.00253557	15.68 KB/S	0.385
1k-4t	60.37 ms	0.00356058	66.26 KB/S	1.096
1k-16t	62.95 ms	0.00366636	254.17 KB/S	4.258
1k-32t	77.18 ms	0.00455239	414.54 KB/S	6.857
1k-64t	135.32 ms	0.00701475	472.87 KB/S	8.889
1k-128t	261.85 ms	0.0104582	488.76 KB/S	11.908
64k-1t	64.59 ms	0.00286986	990.33 KB/S	21.758
64k-4t	61.52 ms	0.00377452	4.15 MB/S	66.184
64k-16t	63.56 ms	0.00396539	16.1 MB/S	251.939
64k-32t	75.95 ms	0.00509964	26.96 MB/S	391.683
64k-64t	132.55 ms	0.00862268	30.9 MB/S	463.305
64k-128t	266.11 ms	0.0118398	30.78 MB/S	671.976
1m-1t	32.17 ms	0.00565897	31.81 MB/S	176.615
1m-4t	29.96 ms	0.0063191	136.69 MB/S	632.447
1m-16t	40.64 ms	0.0200377	403.04 MB/S	797.653
1m-32t	80.21 ms	0.0599666	408.47 MB/S	532.864
1m-64t	169.55 ms	0.085622	386.5 MB/S	745.441
1m-128t	348.26 ms	0.20172	376.35 MB/S	632.207
16m-1t	239.92 ms	0.0499615	68.28 MB/S	319.865
16m-4t	223.3 ms	0.0904987	293.45 MB/S	706.274
16m-16t	394.26 ms	0.35889	664.86 MB/S	709.663
16m-32t	628.91 ms	0.700586	833.62 MB/S	728.33
16m-64t	1055.42 ms	1.26268	993.5 MB/S	804.679
16m-128t	1948.95 ms	2.38641	1.08 GB/S	837.092
64m-1t	488.37 ms	0.166078	134.18 MB/S	384.1
64m-4t	518.64 ms	0.52718	505.4 MB/S	483.174
64m-16t	1061.8 ms	2.23922	987.45 MB/S	454.274
64m-32t	2053.39 ms	4.27337	1.02 GB/S	468.964
64m-64t	3952.32 ms	7.465	1.06 GB/S	497.011
64m-128t	7564.38 ms	14.9165	1.11 GB/S	420.287

4 Storage Nodes

<object size>-<num threads>t	Avg latency using rados gateway and cosbench	Avg throughput using rados gateway and cosbench
1k-1t	60.19 ms	16.11 KB/S
1k-4t	58.68 ms	65.43 KB/S
1k-16t	60 ms	256.09 KB/S
1k-32t	73.02 ms	439.91 KB/S
1k-64t	124.18 ms	509.75 KB/S
1k-128t	239.27 ms	503.33 KB/S
64k-1t	62.95 ms	1.02 MB/S
64k-4t	62.2 ms	4.11 MB/S
64k-16t	62.78 ms	16.3 MB/S
64k-32t	72.61 ms	28.18 MB/S
64k-64t	122.92 ms	33.31 MB/S
64k-128t	236.88 ms	34.57 MB/S
1m-1t	38.87 ms	26.34 MB/S
1m-4t	32.02 ms	127.86 MB/S
1m-16t	39.5 ms	414.67 MB/S
1m-32t	66.75 ms	490.79 MB/S
1m-64t	126.97 ms	516.12 MB/S
1m-128t	248.63 ms	527.14 MB/S
16m-1t	244.58 ms	66.98 MB/S
16m-4t	192.53 ms	340.34 MB/S
16m-16t	343.1 ms	763.98 MB/S
16m-32t	548.17 ms	956.35 MB/S
16m-64t	990.05 ms	1.06 GB/S
16m-128t	1865.8 ms	1.12 GB/S
64m-1t	518.82 ms	126.31 MB/S
64m-4t	499.1 ms	525.17 MB/S
64m-16t	952.81 ms	1.1 GB/S
64m-32t	1850.74 ms	1.13 GB/S
64m-64t	3614.55 ms	1.16 GB/S
64m-128t	7040.89 ms	1.19 GB/S

Conclusions
1. Latency and throughput both increases with increase in number of concurrents requests
2. With increase in the number of storage nodes throughput increases and latency decreases.
3. A single rados gateway is able to utilize the cpu, i/o resources of 3/4 storage nodes when the object size is bigger (> 1M) and also able to saturate the 10Gbps link.
Note: system wide statistics are available of all of these tests.

RECOVERY AND REBALANCING

Adding a new node (4th node on a 3 node cluster)

around 3 million objects, 2845 GB data, 8905 GB used, 260 TB / 268 TB avail

Assuming uniform rebalancing across nodes, around 8904/4 GB of data would be moved to the new node.

Start time : 18:13:00
End time : 19:57:00
Time taken : 01:44:00
Data moved : 2226 GB
Throughput : 365 MB/s

Removing a node (4th node from 4 node cluster)

Assuming uniform rebalancing, around 8904/4 GB of data would be replicated on the remaining nodes.

Start time : 12:40:00
End time: 14:42:00
Time taken : 02:02:00
Data moved : 2226 GB
Throughput : 311 MB/s

Note: system wide statistics are available for all of these tests.

RADOS GATEWAY CONCURRENCY

1 Rados gateway (Read)

<object size>-<num threads>t	Avg latency using rados gateway and cosbench	Avg throughput using rados gateway and cosbench	Avg bandwidth using rados gateway and cosbench
1k-128t	178.28 ms	717.95 op/s	717.95 KB/S
1k-256t	358.75 ms	713.56 op/s	713.56 KB/S
1k-512t	719.5 ms	711.6 op/s	711.6 KB/S
1k-1024t	1449.34 ms	706.53 op/s	706.53 KB/S
1k-2048t	2829.74 ms	723.75 op/s	723.75 KB/S
1m-128t	262.64 ms	487.33 op/s	499.02 MB/S
1m-256t	505.71 ms	506.21 op/s	518.36 MB/S
1m-512t	995.77 ms	514.16 op/s	526.5 MB/S
1m-1024t	1973.14 ms	518.97 op/s	531.42 MB/S

Conclusions:
1. Increasing concurrecy beyond certain point (128 threads) does not increase the throughput.
2. For small objects, the cpu, i/o utilization on storage nodes remains poor.

TODO:
Explore if throughput can be increased for smaller objects or have we hit the cluster limit.

1 Rados gateway (Write)

<object size>-<num threads>t	Avg latency using rados gateway and cosbench	Avg throughput using rados gateway and cosbench	Avg bandwidth using rados gateway and cosbench
1k-128t	569.57 ms	224.66 op/s	224.66 KB/S
1k-256t	1558.53 ms	164.26 op/s	164.26 KB/S
1k-512t	3303.43 ms	155 op/s	155 KB/S
1k-1024t	6733.57 ms	152.08 op/s	152.08 KB/S
1k-2048t	13438.09 ms	152.41 op/s	152.41 KB/S

Conclusions:
1. Increasing concurrecy beyond certain point (128 threads) does not increase the throughput. Infact, for writes, the thoughput is decreasing with more number of threads.
2. For small objects, the cpu, i/o utilization on storage nodes remains poor.

TODO:
1. Explore if throughput can be increased for smaller objects or have we hit the cluster limit.
2. Explore if SSDs for journal will increase throughput for smaller objects

2 Rados gateways (Read)

<object size>-<num threads>t	Avg latency using rados gateway 1	Avg latency using rados gateway 2	Avg throughput using rados gateway 1	Avg throughput using rados gateway 2	Avg bandwidth using rados gateway 1	Avg bandwidth using rados 2ateway 1
1m-128t	472.58 ms	470.68 ms	270.84 op/s	271.94 op/s	277.35 MB/S	278.46 MB/S
1m-256t	939.87 ms	934.11 ms	272.37 op/s	274.05 op/s	278.91 MB/S	280.63 MB/S
1m-512t	1842.8 ms	1821.92 ms	277.83 op/s	281.02 op/s	284.5 MB/S	287.76 MB/S
1m-1024t	3587.13 ms	3536.25 ms	285.46 op/s	289.57 op/s	292.31 MB/S	296.52 MB/S

Conclusion:
Using more than gateway to load the cluster does not result in increased throughput. The numbers are almost similar to that of a sinlge rados gateway. Does it mean that a single rados gateway is not the bottleneck for small reads/writes ?

1 Rados gateway (Read with RGW cache enabled)

<object size>-<num threads>t	Avg latency using rados gateway and cosbench	Avg throughput using rados gateway and cosbench	Avg bandwidth using rados gateway and cosbench
1k-128t	243.24 ms	526.2 op/s	538.83 MB/S
1k-256t	524.37 ms	488.18 op/s	499.9 MB/S
1k-512t	1005.87 ms	508.98 op/s	521.2 MB/S
1k-1024t	1950.51 ms	524.9 op/s	537.49 MB/S
1k-2048t	3818.55 ms	536.54 op/s	549.42 MB/S

Conclusion:
Enabling rados gateway cache decreases the throuhput and increases the latency

Note: system wide statistics are available for all of these tests.